## Slide 1: The ARM Architecture

## Slide 2: Agenda
ARM Introduction
Architecture Extensions
ARM7TDMI-S
Processor Modes
Registers
ARM Vs Thumb
Instruction Set
System Design
Summary

## Slide 3: About Pantech
Started in the Year 2004
Lab equipments and Sensor Interface
Manufacturer of Brainsense EEG Headset
Reconfigurable Algorithms on AI
Manufacture of AI development Boards
Power electronics, Fuel cell and Renewable Energy trainers
www.pantechsolutions.net

## Slide 4: About me
https://www.linkedin.com/in/jeevarajan/
My Primary Expertise
Microcontroller Architecture: 8051,PIC,AVR,ARM,MSP430,PSOC3 DSP Architecture: Blackfin,C2000,C6000,21065L Sharc FPGA: Spartan,Virtex,Cyclone Image Processing Algorithms: Image/Scene Recognition, Machine Learning, Computer Vision, Deep Learning, Pattern Recognition, Object Classification ,Image Retrieval, Image enhancement and denoising. Neural Networks : SVM,RBF,BPN Cryptography :RSA,DES,3DES,Ellipti curve,Blowfish,Diffe Hellman Compilers: Keil,Visual DSP++,CCS, Xilinx Platform studio,ISE, Matlab, Open CV
www.pantechsolutions.net

## Slide 5: Announcement
Attendance Link at 9 pm
Minimum attendance required for an E-Certificate is 27 Days. Attendance link will be valid for 1 hrs. after the event.
For Internship Candidates no attendance required ,it will be accessed from the LMS Portal. (learn.pantechsolutions.net)
Recorded Video Streaming for LAB classes to improve Learning Experience
8051 – 5 Days workshop –use the same attendance form
support.pantechsolutions.net

## Slide 6: What you get on 30 Days Internship

## Slide 7: Mindset Lesson for the Day
“Formal Education will bring you living, Self education will bring your fortune”.-Jim rohn
“ Learn ,Unlearn, Relearn”
The power of repetition
“ Program your subconscious mind for success”

## Slide 8: ARM Ltd.,
Founded in 1990
  Spin out of Acorn Computers
Designs the ARM range of RISC processor
Licenses ARM core for Design Partners
  ARM does not fabricate Silicon on own
  VLSI Technology becomes an investor and the first licensee
Develops technology to assist with ARM Arch.
  Software Tools
  Boards | Debug Hardware | Peripherals
  Application Software | Bus Architecture
Notes: designs to semiconductor partners who fabricate and sell to their customers.

## Slide 9: IP – Intellectual Property
ARM provides hard and soft views to licensees
  RTL and Synthesis Overflow
  GDSII Layout
Licensees have the right to use hard or soft views of the IP
  Soft views include gate level net-list
  Hard view are DSMs
OEMs must use Hard Views
  To protect ARM IP
Notes: 1.Graphic Data Source – IC Fabrication File Formats
-Files normally stored in magnetic strip
-IC Layout Artwork files
2.

## Slide 10: ARM Overview
IP Core
RTL / GDSII Layout
Development Tools
IDE/Debugger
ICE
Silicon Manufacturer
NXP | Atmel | SAMSUNG | INTEL
IAR
KEIL
Realview…

## Slide 11: ARM Overview
Over 200 processor licensees
2500 individual company users of ARM physical IP
50,000 users of ARM development tools
ARM has highly adaptable business models with a range of entry points for all potential customers.

## Slide 12: Markets
The FIVE key markets are:
Embedded Solutions
Smart Cards
Enterprise Solutions
Flash Cards
Printers
Home Solutions
Still Cameras
Digital TV
Automotive
Dashboard Controls
Hard Disks
Set Top Box
Mobile Solutions
Bluetooth
PDA
Smart Phone
Emerging Applications
Gaming
Robot
And much more….
90 % of the mobile handsets use ARM Technology

## Slide 13: Processor Licensee
ARM licenses its microprocessor IP to majority of the semiconductor companies.
Family | Licenses
CortexTM | 69*
ARM11TM | 72
ARM9TM | 253
ARM7TM | 171
Statics info 04/12/2009 – ARM website

## Slide 14: Why ARM ?
Built in architecture extensions
  THUMB®2 - Greatly improved code density
  DSP - Signal process directly in the RISC core
  Jazelle® - Java acceleration
  Trustzone™ - Maximum Security Environment
Core Performance
- Running from 1MHz to 1 GHz with architectural performance enhancements for media and Java.
Wide Support
A wide range of OS, Middleware and tools support an extensive choice of multimedia codec solutions optimized for ARM processors

## Slide 15: Why ARM ?
Low cost of silicon
Architectural features such as Thumb and Thumb-2 core technology reduce code size for minimal footprint and silicon cost.
Rapid Time-to-Market
Low power consumption
ARM microprocessor solutions offer the industries lowest power consumption and MIPS per Watt. These enable long battery life with very advanced features.

## Slide 16: Agenda
ARM Introduction
Architecture Extensions
ARM7TDMI-S
Processor Modes
Registers
ARM Vs Thumb
Instruction Set
System Design
Summary

## Slide 17: Architecture Extensions
Improved Code Density
Improved Performance
Power Efficiency

## Slide 18: Architecture Extensions…
The TrustZone®
  Provide a Trusted Execution Environment (TEE)
  Consistent programming model across platforms and applications
  Hardware backed security environment

## Slide 19: Trust zone – s/w

## Slide 20: Architecture Extensions…
Jazelle®
  Technology to enable Jazelle H/w in any existing JVM
  Full featured multi-tasking Java Virtual Machine JVM
  Enables acceleration of execution environments

## Slide 21: Jazelle
JDBX
  Java Direct Byte-code
  Execution
JRCT
  Java Runtime
  compilation Tool suite

## Slide 22: Apple iPhone Key Design Win for NXP ARM
LPC2211
PMU
12 Logic Parts
5$ – 6 $ content
2007
2008
4 - 5 Mega Units
10 Mega Units

## Slide 23: Significant Design-Win Americas: Q4 2006
Significance | Used LPC900 MCUs to beat Microchip on high volume consumer product | Automation Bank machine can be chosen as world platform by Diebold. Provides stronger security system in this kind of product. |  | 
Customer | Diebold - Procomp |  |  | 
MMS DW Product | LPC2144FBD64-S |  |  | 
Other NXP/MMS part types |  |  |  | 
End Product | Automation Bank Machine |  |  | 
Application | Baking |  |  | 
Quantity (EAU) | 50k units |  |  | 
Value (3yr/5yr auto) | $1.00 mil (3yr) |  |  | 
NXP Competitive Advantage | NXP MCU is most competitive package product solution |  | Sales Engineer | Marcelo Gonçalves

## Slide 24: ARM Partnership Model
Notes: ARM’s business model centres around the principle of partnership. At the centre of this are ARM’s semiconductor partners who design, manufacture and market ARM-compliant products.
Having so many partner companies producing silicon executing the same instruction set is a very important part of ARM’s strength in the market place.
However each of our semiconductor partners bring their own unique strengths to the partnership - each having their own technologies, applications knowledge, product focus, culture, geography, and key customers.
In addition to our partnering with semiconductor companies, we also partner with a large number of other third parties to ensure that operating systems, EDA and software development tools, application software and design services are available for doing ARM based designs.
“ATAP” stands for ARM Technology Access Program. Creates a network of independent design service companies and equips them to deliver ARM-powered designs. Members get access to ARM technology, expertise and support. Members sometimes referred to as “Approved Design Centers”.

## Slide 25: End Products

## Slide 26: Agenda
ARM Introduction
Architecture Extensions
ARM7TDMI-S
Processor Modes
Registers
ARM Vs Thumb
Instruction Set
System Design
Summary

## Slide 27: ARM7 TDMI - S
The ARM7TDMI-S is based on ARM7 Core
  3 Stage Pipeline
  Von-Neumann Architecture
  CPI ~ 1.9
    T – Thumb instruction Sets
    D – includes debug extensions
    M – Enhanced Multipliers
    I – Core has Embedded ICE logic extensions
    S – Fully Synthesizable soft IP

## Slide 28: ARM7 Family
ARM7 Family Includes…
ARM7TDMI
ARM7TDMI-S (ARM v4T)
ARM720T
ARM7EJ-S
T - Thumb® instruction set
T - Thumb® instruction set
T – Thumb
D - Debug extension
M-Enhanced multiplier (32x8)
I-Embedded ICE
D - Debug extension
M-Enhanced multiplier (32x8)
I-Embedded ICE
S – Synthesizable Macro
E – DSP Extension
J – Jazelle®, Java Extension
S – Synthesizable
MMU Included
Uses ARM7TDMI-S CPU

## Slide 29: Bus Width
ARM7 is a 32-bit architecture
Data Paths and Instructions (ARM) are 32 bits wide
Von-Neumann Architecture
  Instructions and Data use same bus
Thumb Mode
  Subset of 16-bit instructions
  Code density optimization

## Slide 30: Thumb State
Set of instructions re-coded into 16 bits
  Improved code density by ~ 30%
  saving program memory space
In Thumb state only the program code is 16-bit wide
  after fetching the 16-bit instructions from memory, they are de-compressed to 32 bit instructions before they are decoded and executed
  all operations are still 32-bit operations

## Slide 31: Data Types and Alignment
Definitions (Little endian or big endian are options):
  Word = 32 bits (four bytes)
  Halfword = 16 bits (two bytes)
  Byte = 8 bits
Word
Word
Halfword
Halfword
Byte
Byte
Byte
Byte
Halfword
Halfword
Byte
Byte
Byte
Byte
Halfword
Halfword
Word
1
2
3
4
1
2
3
4
Word

## Slide 32: Data and Instruction
DATA when used in ARM
  Byte : 8 bits
  Half Word : 16 bits (2 Bytes)
  Word : 32 bits (4 Bytes)
Instruction Set of most ARMs
  32 bits ARM Instruction Set
  16 bits Thumb Instruction Set

## Slide 33: Agenda
ARM Introduction
Architecture Extensions
ARM7TDMI-S
Processor Modes
Registers
ARM Vs Thumb
Instruction Set
System Design
Summary

## Slide 34: Processor Modes
User
Unprivileged Mode
Most tasks run on this mode
FIQ
Entered when a high priority Interrupt is occurred
IRQ
Entered when a low priority interrupt (normal) is occurred
Supervisory
Entered on Reset
Entered on Software Interrupt
Abort
To handle memory access violations
Undefined
To handle un-defined instructions
System
Privileged mode using the same registers as user mode

## Slide 35: Agenda
ARM Introduction
Architecture Extensions
ARM7TDMI-S
Processor Modes
Registers
ARM Vs Thumb
Instruction Set
System Design
Summary

## Slide 36: The Registers
ARM has 37 registers all of which are 32 bits long
  1 dedicated Program Counter
  1 dedicated Current Program Status Register (CPSR)
  5 dedicated Saved Program Status Register (SPSR)
  30 General Purpose Register
The current processor mode governs the access of register banks
  A particular set of r0-r12 registers
  A particular r13 (stack pointer) and r14 (link register, LR)
  The program counter (PC)
  The current program status register (CPSR)
Privileged Mode can access
  A particular SPSR (Saved Program Status Register)
Notes: The ARM architecture provides a total of 37 registers, all of which are 32-bits long. However these are arranged into several banks, with the accessible bank being governed by the current processor mode. We will see this in more detail in a couple of slides. In summary though, in each mode, the core can access:
  a particular set of 13 general purpose registers (r0 - r12).
  a particular r13 - which is typically used as a stack pointer. This will be a different r13 for each mode, so allowing each exception type to have its own stack.
  a particular r14 - which is used as a link (or return address) register. Again this will be a different r14 for each mode.
  r15 - whose only use is as the Program counter.
The CPSR (Current Program Status Register) - this stores additional information about the state of the processor:
And finally in privileged modes, a particular SPSR (Saved Program Status Register). This stores a copy of the previous CPSR value when an exception occurs. This combined with the link register allows exceptions to return without corrupting processor state.

## Slide 37: The ARM Register Set
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
FIQ
IRQ
SVC
Undef
Abort
User Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
FIQ
IRQ
SVC
Undef
Abort
r0
r1
r2
r3
r4
r5
r6
r7
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
IRQ
SVC
Undef
Abort
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
FIQ Mode
IRQ Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
FIQ
SVC
Undef
Abort
r13 (sp)
r14 (lr)
Undef Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
FIQ
IRQ
SVC
Abort
r13 (sp)
r14 (lr)
SVC Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
FIQ
IRQ
Undef
Abort
r13 (sp)
r14 (lr)
Abort Mode
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r15 (pc)
cpsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r13 (sp)
r14 (lr)
spsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
Current Visible Registers
Banked out Registers
User
FIQ
IRQ
SVC
Undef
r13 (sp)
r14 (lr)
Notes: This animated slide shows the way that the banking of registers works. On the left the currently visible set of registers are shown for a particular mode.
On the right are the registers that are banked out whilst in that mode.
Each key press will switch mode:
user -> FIQ ->user -> IRQ -> user ->SVC -> User -> Undef -> User -> Abort and then back to user.
The following slide then shows this in a more static way that is more useful for reference

## Slide 38: Register Organization Summary
User mode r0-r7, r15, and cpsr
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
spsr
FIQ
r8
r9
r10
r11
r12
r13 (sp)
r14 (lr)
r15 (pc)
cpsr
r0
r1
r2
r3
r4
r5
r6
r7
User
r13 (sp)
r14 (lr)
spsr
IRQ
User mode r0-r12, r15, and cpsr
r13 (sp)
r14 (lr)
spsr
Undef
User mode r0-r12, r15, and cpsr
r13 (sp)
r14 (lr)
spsr
SVC
User mode r0-r12, r15, and cpsr
r13 (sp)
r14 (lr)
spsr
Abort
User mode r0-r12, r15, and cpsr
Thumb state
Low registers
Thumb state
High registers
Note: System mode uses the User mode register set
Notes: This slide shows the registers visible in each mode - basically in a more static fashion than the previous animated slide that is more useful for reference.
The main point to state here is the splitting of the registers in Thumb state into Low and High registers.
ARM register banking is the minimum necessary for fast handling of overlapping exceptions of different types (e.g. ABORT during SWI during IRQ). For nested exceptions of the same type (e.g. re-entrant interrupts) some additional pushing of registers to the stack is required.

## Slide 39: Program Status Registers
Condition code flags
  N = Negative result from ALU
  Z = Zero result from ALU
  C = ALU operation Carried out
  V = ALU operation overflowed
Sticky Overflow flag - Q flag
  Architecture 5TE/J only
  Indicates if saturation has occurred
J bit
  Architecture 5TEJ only
  J = 1: Processor in Jazelle state
Interrupt Disable bits.
  I = 1: Disables the IRQ.
  F = 1: Disables the FIQ.
T Bit
  Architecture xT only
  T = 0: Processor in ARM state
  T = 1: Processor in Thumb state
Mode bits
  Specify the processor mode
27
31
N Z C V Q
28
6
7
I F T mode
16
23
8
15
5
4
0
24
f
s
x
c
U n d e f i n e d
J
Notes: Green psr bits are only in certain versions of the ARM architecture
ALU status flags (set if "S" bit set, implied in Thumb state).
Sticky overflow flag (Q flag) is set either when
  saturation occurs during QADD, QDADD, QSUB or QDSUB, or
  the result of SMLAxy or SMLAWx overflows 32-bits
Once flag has been set can not be modified by one of the above instructions and must write to CPSR using MSR instruction to cleared
PSRs split into four 8-bit fields that can be individually written:
Control (c) bits 0-7
Extension (x) bits 8-15 Reserved for future use
Status (s) bits 16-23 Reserved for future use
Flags (f) bits 24-31
Bits that are reserved for future use should not be modified by current software. Typically, a read-modify-write strategy should be used to update the value of a status register to ensure future compatibility. Note that the T/J bits in the CPSR should never be changed directly by writing to the PSR (use the BX/BXJ instruction to change state instead).
However, in cases where the processor state is known in advance (e.g. on reset, following an interrupt, or some other exception), an immediate value may be written directly into the status registers, to change only specific bits (e.g. to change mode).
New ARM V6 bits now shown.

## Slide 40: Exception Handling
Vector Table
When an exception occurs, the ARM:
  Copies CPSR into SPSR_<mode>
  Sets appropriate CPSR bits
    Change to ARM state
    Change to exception mode
    Disable interrupts (if appropriate)
  Stores the return address in LR_<mode>
  Sets PC to vector address
To return, exception handler needs to:
  Restore CPSR from SPSR_<mode>
  Restore PC from LR_<mode>
This can only be done in ARM state.
Vector table can be at 0xFFFF0000 on ARM720T and on ARM9/10 family devices
FIQ
IRQ
(Reserved)
Data Abort
Prefetch Abort
Software Interrupt
Undefined Instruction
Reset
0x1C
0x18
0x14
0x10
0x0C
0x08
0x04
0x00
Notes: Exception handling on the ARM is controlled through the use of an area of memory called the vector table. This lives (normally) at the bottom of the memory map from 0x0 to 0x1c. Within this table one word is allocated to each of the various exception types.
This word will contain some form of ARM instruction that should perform a branch. It does not contain an address.
Reset - executed on power on
Undef - when an invalid instruction reaches the execute stage of the pipeline
SWI - when a software interrupt instruction is executed
Prefetch - when an instruction is fetched from memory that is invalid for some reason, if it reaches the execute stage then this exception is taken
Data - if a load/store instruction tries to access an invalid memory location, then this exception is taken
IRQ - normal interrupt
FIQ - fast interrupt
When one of these exceptions is taken, the ARM goes through a low-overhead sequence of actions in order to invoke the appropriate exception handler. The current instruction is always allowed to complete (except in case of Reset).
IRQ is disabled on entry to all exceptions; FIQ is also disabled on entry to Reset and FIQ.

## Slide 41: Agenda
ARM Introduction
Architecture Extensions
ARM7TDMI-S
Processor Modes
Registers
ARM Vs Thumb
Instruction Set
System Design
Summary

## Slide 42: Thumb vs. ARM
Thumb
State
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13 (SP)
r14 (LR)
r15 (PC)
CPSR
SPSR
r0
r1
r2
r3
r4
r5
r6
r7
r13 (SP)
r14 (LR)
r15 (PC)
CPSR
SPSR
ARM
State
Thumb state
Low registers
Thumb state
High registers

## Slide 43: Registers in Thumb State
The Thumb state register set is a subset of the ARM state set. The programmer has direct access to:
  eight general registers r0 - r7
  the program counter PC
  a Stack pointer SP
  a Link register LR
  the current program status register CPSR
In Thumb state, the high registers (r8 - r12) are not part of the standard register set. The assembly language programmer has limited access to them, but can use them for fast temporary storage

## Slide 44: Program Counter (r15)
When the processor is executing in ARM state:
  All instructions are 32 bits wide
  All instructions must be word aligned
  Therefore the pc value is stored in bits [31:2] with bits [1:0] undefined (as instruction cannot be halfword or byte aligned).
When the processor is executing in Thumb state:
  All instructions are 16 bits wide
  All instructions must be halfword aligned
  Therefore the pc value is stored in bits [31:1] with bit [0] undefined (as instruction cannot be byte aligned).
When the processor is executing in Jazelle state:
  All instructions are 8 bits wide
  Processor performs a word access to read 4 instructions at once
Notes: ARM is designed to efficiently access memory using a single memory access cycle. So word accesses must be on a word address boundary, halfword accesses must be on a halfword address boundary. This includes instruction fetches.
Point out that strictly, the bottom bits of the PC simply do not exist within the ARM core - hence they are ‘undefined’. Memory system must ignore these for instruction fetches.
In Jazelle state, the processor doesn’t perform 8-bit fetches from memory. Instead it does aligned 32-bit fetches (4-byte prefetching) which is more efficient. Note we don’t mention the PC in Jazelle state because the ‘Jazelle PC’ is actually stored in r14 - this is technical detail that is not relevant as it is completely hidden by the Jazelle support code.

## Slide 45: Agenda
ARM Introduction
Architecture Extensions
ARM7TDMI-S
Processor Modes
Registers
ARM Vs Thumb
Instruction Set
System Design
Summary

## Slide 46: Instruction Set
All instructions are 32-bits long
Many instructions execute in a single cycle
Instructions are conditionally executed
ARM is a load / store architecture
  via registers => RISC
Load or store multiple registers in a single instruction
    using <register list>

## Slide 47: Conditional Execution
Mnemonic | Description
EQ | Equal
NE | Not equal
CS / HS | Carry Set / Unsigned higher or same
CC / LO | Carry Clear / Unsigned lower
MI | Negative
PL | Positive or zero
VS | Overflow
VC | No overflow
HI | Unsigned higher
LS | Unsigned lower or same
GE | Signed greater than or equal
LT | Signed less than
GT | Signed greater than
LE | Signed less than or equal
AL | Always (normally omitted)

## Slide 48: Thumb Instruction Set (1)
Instruction Types
  Branch
    Unconditional ± 2KBytes
    Conditional ± 256Bytes
    Branch with Link ± 4MBytes (2 Instructions!)
    Branch and exchange change to ARM state if Rm[0] = 0
    Branch and exchange with Link
  Data Processing
    Subset of ARM data processing instructions
    Not conditionally executed (but some update flags)

## Slide 49: ARM and Thumb Interworking
Switch between ARM state and Thumb state using BX instruction
  In ARM state: BX<condition> Rn
  In Thumb state: BX Rn
Rn
n: 0-15
0
1
31
0
0
1
31
Destination
address
ARM / Thumb selection
0: ARM state
1: Thumb state
BX
Notes: The BX (Branch and Exchange) instruction branches to an address held in a register Rm, with an optional switch to Thumb execution. The branch target address is the value of register Rm, with its bit[0] forced to zero. The instruction set to be used at the branch target is chosen by setting the CPSR T bit to bit[0] of Rm.

## Slide 50: Instruction Pipeline
The ARM7TDMI-S core uses a pipeline
  Increase the speed of the flow of instructions
  Enables several operations to take place simultaneously
  Program Counter (PC) points to instruction being fetched rather than that being executed
During normal pipelined operation
  An instruction x is executed
  Instruction (x-1) is being decoded
  Instructino (x-2) is being fetched

## Slide 51: 3-Stage Instruction Pipeline
Fetch
Decode
Execute
ARM
PC
PC - 4
PC - 8
Thumb
PC
PC - 2
PC - 4
Instruction Fetched from Memory
Thumb only: Thumb instruction decompressed to ARM instruction Instruction decoded
Registers read from Register Bank, Shift and ALU operations performed, Registers written back to Register Bank

## Slide 52: Optimal Pipelining
In this example it takes 6 clock cycles to execute 6 instructions
All operations are on registers (single cycle instructions)
Clock cycles per instruction (CPI) = 1
2
3
5
7
Cycle
1
4
6
8
Fetch
Decode
Execute
Fetch
Decode
Execute
Fetch
Decode
Execute
Fetch
Decode
Execute
Fetch
Decode
Execute
Fetch
Decode
Execute
Fetch
Decode
Fetch
ADD
SUB
MOV
AND
ORR
EOR
CMP
RSB

## Slide 53: Branch Pipeline Example
Branches break the pipeline
Example in ARM state
1
2
4
6
Cycle
3
5
7
Fetch
Decode
Execute
Fetch
Decode
Fetch
Fetch
Decode
Execute
BL
X
X
ADD
SUB
MOV
Linkret
Adjust
Fetch
Decode
Execute
Fetch
Fetch
AND
0x8000
0x8004
0x8008
0x8FEC
0x8FF0
0x8FF4
0x8FF8
Decode

## Slide 54: Agenda
ARM Introduction
Architecture Extensions
ARM7TDMI-S
Processor Modes
Registers
ARM Vs Thumb
Instruction Set
System Design
Summary

## Slide 55: Example ARM based System
RAM
16 bit wide
RAM
32 bit wide
ARM core
Peripherals
I / O
ROM
8 bit wide
Interrupt Controller

## Slide 56
Advanced Microcontroller Bus Architecture
  on-chip interconnect
  established, open specification
  framework for SoC designs
  enabler for IP reuse
  ‘digital glue’ that binds IP cores together

## Slide 57: Example AMBA System
High-bandwidth on-chip RAM
ARM core
DMA Bus Master
High-bandwidth Memory Interface
UART
Timer
Keypad
Display
APB
APB Bridge
RTC
I/O
AHB

## Slide 58: AHB and APB / VPB
Advanced High-Performance Bus
  high-performance
  pipelined
  fully-synchronous backplane
  multiple bus masters
Advanced Peripheral Bus / VLSI Peripheral Bus
  low-power
  non-pipelined
  simple interface
  wait support (VPB)

## Slide 59: ARM

## Slide 60: ARM Debug Architecture
EmbeddedICE Logic
  Provides breakpoints and processor/system access
JTAG interface (ICE)
  Converts debugger commands to JTAG signals
Embedded trace Macrocell (ETM)
  Compresses real-time instruction and data access trace
  Contains ICE features (trigger & filter logic)
Trace port analyzer (TPA)
  Captures trace in a deep buffer
ARM
core
ETM
TAP
controller
Trace Port
JTAG port
Ethernet
Debugger (+ optional
trace tools)
EmbeddedICE
Logic
Notes: Debugger trace tools
  Have copy of the code image
  Configure ETM trace via JTAG
  Receive compressed trace from ETM
  Decompress ETM trace using code image

## Slide 61: Why ARM?
ARM7 is an open architecture
Already the preferred 32-bit solution in Automotive, Communication and Industrial markets.
Same tools for all ARM7 of different manufacturer. Often the same tools can be used for ARM9/10/11. Customers can save money
ARM is a scalable and uniform architecture. ARM7 is binary code compatible with ARM9/10. customer can chose the right product for its target application saving time due to the reduced learning curve.

## Slide 62: References
www.arm.com
http://www.arm.com/markets/
http://in.youtube.com/watch?v=4VRtujwa_b8
  ARM Webinars | ARM Video Search
http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.set.appnotes/

## Slide 63: References

## Slide 64: Summary
ARM Company Overview | Introduction
Various Architecture Extensions
Different Processor Modes
Internal Registers Usages
ARM Vs Thumb
Instruction Set

## Slide 65: Questions ?

## Slide 66
Thank You!