## Slide 1: Introduction to Cortex M4 Architecture –LPC4088
EMBEDDED SYSTEM DESIGN & IoT-Master Class
DAY 16

## Slide 2
What You will learn Today?
Embedded System Design using Cortex M4
LPC4088 Block Diagram and Features
Registers
Led Blinking

## Slide 3: Mindset Lesson for the Day
When You Are Able To master Your Senses, You Will Master Your Life

## Slide 4: Embedded Sytem Design using Cortex M4-LPC4088

## Slide 5: Types of Connectors
RS232
VGA
HDMI
PARALLEL PORT

## Slide 6: Types of USB Connectors

## Slide 7: Connectors
PCB TERMINAL BLOCK CONNECTORS
Berg strips –Male and Female
PS2 Connectors
BOX Connectors
RMC Connectors

## Slide 8: Active & Passive Components

## Slide 9: Switches
DIP Switch
Slide Switch
Tactile push button switch

## Slide 10: Crystal and Oscillator

## Slide 11: LPC4088 –Cortex M4
The Cortex-M4 processor is a high-performance 32-bit processor with a 3-stage pipeline
Harvard architecture with separate local instruction and data buses, as well as a third bus
with slightly lower performance for peripherals.
The Cortex-M4 uses the Thumb® instruction set, providing high code density and reduced program memory requirements.
The Cortex-M4 CPU also includes an internal prefetch unit that supports speculative branches.
The LPC408x/407x is targeted to operate at up to a 120 MHz CPU frequency under worst case commercial conditions

## Slide 12: LPC4088 BLOCK DIAGRAM

## Slide 13: ARM CORTEX M4 Features
running at frequencies of up to 120 MHz
Memory Protection Unit (MPU)
Nested Vectored Interrupt Controller (NVIC)
Hardware floating-point unit (not all versions)
Non-maskable Interrupt (NMI) input
JTAG and Serial Wire Debug (SWD)
Embedded Trace Macrocell (ETM)
System tick timer
Memory
up to 512 kB on-chip Flash (ISP and IAP capabilities)
up to 96 kB on-chip SRAM includes
up to 4032 byte on-chip EEPROM

## Slide 14
LCD controller (not all versions)
External Memory Controller (EMC) (not all versions)
General Purpose DMA controller (GPDMA)
Serial interfaces
Quad SPI Flash Interface (SPIFI)
Ethernet MAC with MII/RMII interface (not all versions)
USB 2.0 full-speed dual port device/host/OTG controller (not all versions)
up to 5 UARTs
3 SSP controllers
I2S (Inter-IC Sound) interface
CAN controller with 2 channels
Digital peripherals
SD/MMC memory card interface (not all versions)
Up to 165 General Purpose I/O (GPIO) pins
4 general purpose timers/counters
Quadrature encoder interface (not all versions)
2 standard PWM/timer blocks
One motor control PWM
Real-Time Clock (RTC)
Event Recorder
Windowed Watchdog Timer (WWDT)
CRC Engine block

## Slide 15
Analog peripherals
- 12-bit Analog-to-Digital Converter (ADC)
- 10-bit Digital-to-Analog Converter (DAC)
- 2 analog comparators (not all versions)
Power control
- 4 reduced power modes (Sleep, Deep-sleep, Power-down, Deep power-down)
- Brownout detect with separate threshold
- On-chip Power-On Reset (POR).
Clock generation
Clock output function that can reflect various clocks
On-chip crystal oscillator (1 MHz to 25 MHz)
12 MHz Internal RC oscillator (IRC)
on-chip PLL allows CPU operation up to the max. CPU rate
dedicated PLL may be used for USB interface

## Slide 16: Power Supply Design

## Slide 17: FT232 Interface and ISP Programming

## Slide 18: LPC4088

## Slide 19: Crystal

## Slide 20: JTAG

## Slide 21: Reset and Interrupt

## Slide 22: ADC Interface

## Slide 23: LED Interface

## Slide 24: Slide Switch Interface

## Slide 25: RS232 Interface

## Slide 26: Keypad Interface

## Slide 27: Stepper Motor Interface

## Slide 28: Buzzer Interface

## Slide 29: I2C EEPROM

## Slide 30: LCD Interface

## Slide 31: LED Blinking demo
#include "LPC407x_8x_177x_8x.h"
void delay_ms(long ms);
int main(void)
{
//1. Set the PCGPIO bit
LPC_SC->PCONP |= (1<<15);
//2. Configure pins P4.0 to P4.7 as GPIO pins
LPC_IOCON->P4_0 = 0;
LPC_IOCON->P4_1 = 0;
LPC_IOCON->P4_2 = 0;
LPC_IOCON->P4_3 = 0;
LPC_IOCON->P4_4 = 0;
LPC_IOCON->P4_5 = 0;
LPC_IOCON->P4_6 = 0;
LPC_IOCON->P4_7 = 0;
//3. Configure the pins P4.0 to P4.7 as output
LPC_GPIO4->DIR= 0xFF;
while(1)
{
//4. Send a High
LPC_GPIO4->PIN= 0xFF;
//5.Pause the system for few milliseconds
delay_ms(500);
//6.Send a low
LPC_GPIO4->PIN= 0x00;
//7.Pause the system for few milliseconds
delay_ms(500);
}
}

## Slide 32: Delay
void delay_ms(long ms) // delay 1 ms per count @ CCLK 120 MHz
{
long i,j;
for (i = 0; i < ms; i++ )
for (j = 0; j < 26659; j++ );
}

## Slide 33: Thank You